Coastal Bronze         60-350, 60-360  Drop Bar Lever Latch            Installation Instructions

Work required:

Multiple holes and arrangement is required in gate or door to mount this hardware.

Parts for 60-350 & 60-360

1x  SPINDLE

1x  LEVER NO DROP BAR

1x  LEVER WITH DROP BAR

1x  FLAT CATCH PLATE or MORTISE CATCH for Drop bar

10x  SCREWS--12 round head mounting screws

Tools required for mounting:

- Electric drill

- 1/8” diameter drill

- 1/2”, 3/4”, 1-1/4” diameter wood bit

- Screw driver with blade end

- Nail Punch

INSTALLATION

Gate or door should be hung on its hinges before installing latch.  There should be between a 1/4” and 1/8” vertical clearance gap between the gate or door and its post or frame.

The top of the plate should be set approximately 35” to 60” from the ground depending on personal preference.

Determine the side of the gate or door that swings toward you as you open the gate or door.  This will be the “LATCH SIDE”

1) ON “LATCH SIDE”

LOCATE THE LEVER POSITION—Take the lever drop bar side template and fold the paper along the line.  Make sure that the line on the template is just showing on the face of the gate or door and not on the edge. Tape the template into place. Take a nail punch and mark into the wood the four crosses on the template. Now follow the drilled holes in alphabetical order.

A)  Drill a 1/8” pilot hole “STRAIGHT” through the gate or door.

- Drill a 3/4” hole 3/8” deep.

- Drill a 1-1/4” hole 3/8” deep.

- Drill a 1/2” hole 3/8” deep.

- Drill a 1-1/4” hole 3/8” deep.

2) ON “NON-LATCH SIDE”

Take the lever side template and fold the paper along the line.  Make sure that the line on the template is just showing on the face of the gate or door and not on the edge. Align the pilot hole that was drilled through the gate or door with the “I” cross on the template. Tape the template into place. Take a nail punch and mark into the wood the two crosses on the template. Now follow the drilled holes in alphabetical order.

- Drill a 3/4” hole 3/8” deep.

- Drill a 3/4” hole 3/8” deep.

- Drill a 1/2” hole 3/8” deep.

- Drill a 1-1/4” hole 3/8” deep.

- Drill a 3/4” hole, following the pilot hole, through the gate or door. (latch side template)

3) MOUNTING THE HARDWARE

Mount the drop bar side first. Make sure the edge of the plate is sitting on the edge of the gate or door and the plate is sitting flat on the gate or door. Mark the four screw holes with the nail punch. Using the 1/8” drill, tap each of the four holes. Mount the latch side hardware to the gate or door. Insert the spindle through the gate or door in the “I” hole of the template.  Mount the non-drop bar side second. Make sure the spindle connects into the lever.  Make sure the plate is straight and the plate is sitting flat on the gate or door. Mark the four screw holes with the nail punch. Using the 1/8” drill, tap each of the four holes. Mount the non-latch side hardware to the gate or door and make sure all parts work freely, tighten screws.

4) MOUNT THE CATCH PLATE on the vertical post or frame at the rest position of the DROP BAR with 2 remaining screws. Make sure that there is no more than ¾” between the catch and the edge of plate.  When either lever is turned, the DROP BAR will lift to clear the catch.

5) MOUNT THE MORTISE CATCH PLATE on the vertical post or frame at the rest position of the DROP BAR with 3 remaining screws. Make sure that there is no more then ¾” between the catch and the edge of plate.  When either lever is turned, the DROP BAR will lift to clear the catch.